## Slide 1: AMBA APB
Digital VLSI Design
Actor: Hoang Bao Long

## Slide 2: 1. Specifications
Digital VLSI Design
Actor: Hoang Bao Long

## Slide 3: 1. Specifications
The Advanced Microcontroller Bus Architecture (AMBA) specification defines an on-chip communications standard for designing high-performance embedded microcontrollers.
Four distinct buses are defined within the AMBA specification:
The Advanced High-performance Bus (AHB)
The Advanced System Bus (ASB)
The Advanced Peripheral Bus (APB).
The Advanced eXtensible Interface (AXI)
1.1. Overview of AMBA Protocol

## Slide 4: 1. Specifications
AMBA AHB | AMBA ASB | AMBA APB
High performance | High performance | Low power
Pipelined operation | Pipelined operation | Latched address and control
Multiple bus masters | Multiple bus masters | Simple interface
Burst transfers |  | Suitable for many peripherals
Split transactions |  | 
1.1. Overview of AMBA Protocol

## Slide 5: 1. Specifications
1.2. Key features of the AMBA Advanced Peripheral Bus (APB)
Low-cost interface: APB is designed with a simple architecture that minimizes hardware resources and implementation cost.
Non-pipelined operation: Transfers are performed sequentially without overlapping phases.
Synchronous protocol: All APB transactions are synchronized to the system clock.
Low power consumption: The non-pipelined and simple transfer mechanism helps reduce power usage, making APB suitable for peripheral devices.
Low bandwidth, optimized for control register access APB is intended for accessing programmable control registers rather than high-throughput data transfers.

## Slide 6: 1. Specifications
1.2. Key features of the AMBA Advanced Peripheral Bus (APB)
Designed for simple peripheral devices: Commonly used for peripherals such as GPIO, Timers, UART, SPI, and I2C.
Accessed through an APB bridge: APB peripherals are typically connected to the main system bus through a bridge (e.g., AXI-to-APB bridge).
Clear Requester–Completer model:
The APB bridge acts as the Requester, initiating transactions.
The peripheral device acts as the Completer, responding to requests.
Well-suited for AMBA-based multi-bus systems: APB integrates seamlessly with other AMBA buses such as AXI and AHB via bridges.

## Slide 7: 1. Specifications
1.2. Key features of the AMBA Advanced Peripheral Bus (APB)

## Slide 8: 1. Specifications
1.3. AMBA APB signals
Block Diagram & Signal Description of APB

## Slide 9: 1. Specifications
1.3. AMBA APB signals
Signal | Source | Width | Description
PCLK | Clock Source | 1 | Clock. The rising edge of PCLK times all transfer on the APB
PRESETn | System Bus | 1 | Reset. The APB reset signal is active LOW. This signal is normally connected directly to the system bus reset signal.
PADDR | APB bridge | ADDR_WIDTH | Address. This is APB address bus. It can be up to 32 bits wide and is driven by the peripheral bus bridge unit.
PPROT | APB bridge | 3 | Protection type. This signal indicates the normal, privileged, or secure protection level of the transaction and whether the transaction is a data access or an instruction access.
PSELx | APB bridge | 1 | Slave select signal, there will be one PSEL signal for each slave connected to master.. It’s an active high signal.
PENABLE | APB bridge | 1 | Enable. It indicates the 2nd cycle of a data transfer. It’s an active high signal.

## Slide 10: 1. Specifications
1.3. AMBA APB signals
Signal | Source | Width | Description
PWRITE | APB bridge | 1 | Direction. PWRITE indicates an APB write access when HIGH and an APB read access when LOW.
PWDATA | APB bridge | DATA_WIDTH | Write data. Write data bus from Master to Slave, can be up to 32 bit wide
PSTRB | APB bridge | DATA_WIDTH/8 | Write strobe. PSTRB indicates which byte lanes to update during a write transfer. There is one write strobe for each 8 bits of the write data bus. PSTRB[n] corresponds to PWDATA[(8n + 7):(8n)]. PSTRB must not be active during a read transfer.
PREADY | Slave Interface | 1 | It is used by the slave to include wait states in the transfer. i.e. whenever slave is not ready to complete the transaction, it will request the master for some time by de-asserting the PREADY.
PSLVERR | Slave Interface | 1 | Indicates the Success or failure of the transfer. HIGH indicates failure and LOW indicates Success
PRDATA | Slave Interface | DATA_WIDTH | Read data us from Slave to Master, can be up to 32 bit wide

## Slide 11: 1. Specifications
1.4. APB Transfer – Write Transfers (without wait state)
At T1, a write transfer with address PADDR,PWDATA,PWRITE and PSEL starts.
They will registered at the next rising edge of PCLK, T2.
This is Setup Phase of Transfer.
After T2, PENABLE and PREADY are registered at the rising edge of PCLK.
When asserted, PENABLE indicates starting of ACCESS Phase
When asserted, PREADY indicates that slave can complete the transfer at the next rising edige of PCLK.
PADDR, PDATA and control signals all should remain valid till the transfer completes at T3.
PENABLE signal will be de-asserted at the end of transfer.
PSEL is also de-asserted, if next transfer is not to the same slave.

## Slide 12: 1. Specifications
1.4. APB Transfer – Write Transfers (with wait state)
During the ACCESS Phase, when PENABLE is high, the slave extends the transfer by driving PREADY low.
The PADDR, PWRITE, PSEL, PENABLE, PWDATA, PSTRB, PPROT signals should remain unchanged while PREADY is low
PREADY can take any value when PENABLE is low.
It is recommended that the address and write signals are not changed immediately after a transfer, but remain stable until another access occurs.

## Slide 13: 1. Specifications
1.4. APB Transfer – Write strobes
PSTRB enables sparse data transfer on the write data bus. Each PSTRB corresponds to 1 byte of the write data bus. When asserted HIGH, PSTRB indicates that the corresponding byte lane of the write data bus contains valid information.
There is one write strobe for each 8 bits of the write data bus, so PSTRB[n] corresponds to PWDATA[(8n + 7):(8n)].

## Slide 14: 1. Specifications
1.4. APB Transfer – Write strobes
PSTRB is an optional signal. An APB peripheral might support a limited set of access types, which must be documented for the programmer. This means that all combinations of PSTRB presence might be compatible, if this document states that sparse writes are not supported.
PSTRB | Completer: signal not present | Completer: signal present
Requester: signal not present | Compatible. Sparse writes are not supported. | Compatible. All write data byte lanes are valid for a write. Tie the PSTRB inputs to the PWRITE output from the Requester.
Requester: signal present | Compatible. Sparse writes are not supported. | Compatible.

## Slide 15: 1. Specifications
1.4. APB Transfer – Read Transfers (without wait state)
At T1, a READ transfer with address PADDR, PWRITE and PSEL starts.
They will be registered at rising edge of PCLK.
This is SETUP Phase of the transfer.
After T2, PENABLE and PREADY are registered at the rising edge of PCLK.
When asserted, PENABLE indicates the starting of ACCESS phase.
When asserted, PREADY indicates that slave can complete the transfer at next rising edge of PCLK by providing the data on PRDATA.
Slave must provide the data before the end of read transfer. i.e. before T3.

## Slide 16: 1. Specifications
1.4. APB Transfer – Read Transfers (with wait state)
During the ACCESS Phase, when PENABLE is high, the slave extends the transfer by driving PREADY low.
The PADDR, PWRITE, PSEL, PENABLE, PPROT signals should remain unchanged while PREADY is low

## Slide 17: 1. Specifications
1.4. APB Transfer – Error response
Whenever there is a problem in the transfer, Slave indicates the error response for the transfer by asserting the PSLVERR signal. PSLVERR is only considered valid during the last cycle f and APB transfer, when PSEL, PENABLE and PREADY are all HIGH. It is recommended, but not mandatory that you drive PSLVERR low when it is not being sampled.
Transactions that receive an error response, might or might not have changed the state of peripheral. For example, If APB master performs a write transaction to an APB slave and received an error response, it is not guaranteed that the data is not written on the slave peripheral.

## Slide 18: 1. Specifications
1.4. APB Transfer – Error response
Write transfer
Read transfer

## Slide 19: 1. Specifications
1.4. APB Transfer – Protection until support
To support complex system designs, it is often necessary for both the interconnect and other devices in the system to provide protection against illegal transactions. It is provided by Protection Unit in APB Protocol. The signals indicating the protection unit are PPROT[2:0].
PPROT | Protection | Description | Comments
PPROT[0] | Normal or Privileged | PPROT[0] is used by Requesters to indicate processing mode. A privileged processing mode typically has a greater level of access within a system. | LOW indicates normal access. HIGH indicates privileged access.
PPROT[1] | Secure or Non-secure | PPROT[1] is used in systems where a greater degree of differentiation between processing modes is required. | LOW indicates secure access. HIGH indicates non-secure access
PPROT[2] | Data or Instruction | PPROT[2] gives an indication if the transaction is a data or instruction access. The transaction indication is provided as a hint and might not be accurate in all cases. | LOW indicates data access. HIGH indicates instruction access.

## Slide 20: 1. Specifications
1.4. APB Operation States
IDLE | This is the default state of the APB interface.
SETUP | When a transfer is required, the interface moves into the SETUP state, where the appropriate select signal, PSELx, is asserted. The interface only remains in the SETUP state for one clock cycle and always moves to the ACCESS state on the next rising edge of the clock.

## Slide 21: 1. Specifications
1.4. APB Operation States
ACCESS | PENABLE is asserted in the ACCESS state. During the transition from SETUP to ACCESS and throughout the ACCESS state, the following signals must remain stable: PADDR, PPROT, PWRITE, PSTRB, PAUSER, PWUSER, and PWDATA (for write transfers only). The exit from the ACCESS state depends on PREADY from the Completer: if PREADY is LOW, the bus stays in ACCESS; if PREADY is HIGH, the bus leaves ACCESS and returns to IDLE or moves directly to SETUP for the next transfer.

## Slide 22: 2. Design Specifications
Digital VLSI Design
Actor: Hoang Bao Long

## Slide 23: 2. Design Specifications
APB Interface
2.1. APB Wrapper

## Slide 24: 2. Design Specifications
APB Master block
2.2. APB Master

## Slide 25: 2. Design Specifications
APB Slave block
2.3. APB Slave

## Slide 26: 2. Design Specifications
Signal | Source | Width | Description
TRANS | System BUS | 1 | Start signal. When the TRANS signal is set to HIGH, the system will begin operation. This signal may remain active for one clock cycle or multiple cycles.
READ | System BUS | 1 | Read signal.
WRITE | System BUS | 1 | Write signal.
APB_WRITE_PADDR | System BUS | ADDR_WIDTH | Address. This is the APB write address used by the APB master to write data to the slave. The address can be up to 32 bits wide.
APB_WRITE_DATA | System BUS | DATA_WIDTH | Data Write. This is the data sent from the APB master to the APB slave during a write operation. The data width can be up to 32 bits.
APB_READ_PADDR | System BUS | ADDR_WIDTH | Address. This is the APB read address used by the APB master to read data from the slave. The address can be up to 32 bits wide.
APB_READ_DATA_OUT | System BUS | DATA_WIDTH | Data Out. This is the data which is read from slave. The data width can be up to 32 bits.
2.4. APB Signals

## Slide 27: 2. Design Specifications
Signal | Source | Width | Description
TRANS | System BUS | 1 | Start signal. When the TRANS signal is set to HIGH, the system will begin operation. This signal may remain active for one clock cycle or multiple cycles.
READ | System BUS | 1 | Read signal.
WRITE | System BUS | 1 | Write signal.
APB_WRITE_PADDR | System BUS | ADDR_WIDTH | Address. This is the APB write address used by the APB master to write data to the slave. The address can be up to 32 bits wide.
APB_WRITE_DATA | System BUS | DATA_WIDTH | Data Write. This is the data sent from the APB master to the APB slave during a write operation. The data width can be up to 32 bits.
APB_READ_PADDR | System BUS | ADDR_WIDTH | Address. This is the APB read address used by the APB master to read data from the slave. The address can be up to 32 bits wide.
APB_READ_DATA_OUT | System BUS | DATA_WIDTH | Data Out. This is the data which is read from slave. The data width can be up to 32 bits.
2.4. APB Signals

## Slide 28: 2. Design Specifications
Signal | Source | Width | Description
PWRITE | APB bridge | 1 | Direction. PWRITE indicates an APB write access when HIGH and an APB read access when LOW.
PWDATA | APB bridge | DATA_WIDTH | Write data. Write data bus from Master to Slave, can be up to 32 bit wide
PSTRB | APB bridge | DATA_WIDTH/8 | Write strobe. PSTRB indicates which byte lanes to update during a write transfer. There is one write strobe for each 8 bits of the write data bus. PSTRB[n] corresponds to PWDATA[(8n + 7):(8n)]. PSTRB must not be active during a read transfer.
PREADY | Slave Interface | 1 | It is used by the slave to include wait states in the transfer. i.e. whenever slave is not ready to complete the transaction, it will request the master for some time by de-asserting the PREADY.
PSLVERR | Slave Interface | 1 | Indicates the Success or failure of the transfer. HIGH indicates failure and LOW indicates Success
PRDATA | Slave Interface | DATA_WIDTH | Read data us from Slave to Master, can be up to 32 bit wide
2.4. APB Signals

## Slide 29: 2. Design Specifications
2.5. APB Operation waveform
APB Write transfer without waiting state
APB Read transfer without waiting state

## Slide 30: 2. Design Specifications
2.5. APB Operation waveform
APB Write with Slave 1 access
APB Read with Slave 1 access

## Slide 31: 2. Design Specifications
2.5. APB Operation waveform
APB Write transfer with waiting state
APB Read transfer with waiting state

## Slide 32: 2. Design Specifications
2.5. APB Operation waveform
APB Write with address range error
APB Read with address range error

## Slide 33: 2. Design Specifications
2.5. Design Spec – APB Master
APB Master FSM

## Slide 34: 2. Design Specifications
2.5. Design Spec – APB Slave
BUS Signals | Name | Descriptions
PADDR[31] | Slave Select Bit | Used to select the target slave. 0 selects Slave 0; 1 selects Slave 1.
PADDR[30:2] | Memory Address | These bits represent the internal memory index (Word-aligned). They are used to access specific data entries within the slave's memory array.
PADDR[1:0] | Waiting Count | These bits determine the number of wait states (delay cycles) the Slave will force the Master to wait before completing the transaction.

## Slide 35: 2. Design Specifications
2.5. Design Spec – APB Slave
APB Slave Memory
APB Waiting State Controller
APB Signal Controller

## Slide 36: 3. Design Verification
Digital VLSI Design
Actor: Hoang Bao Long

## Slide 37: 3. Design Verification
3.1. Verification Plans

## Slide 38: 3. Design Verification
3.2. Testbench environment

## Slide 39: 3. Design Verification
3.2. Testbench environment

## Slide 40: 3. Design Verification
3.2. Testbench environment

## Slide 41: 4. Verification Results
Digital VLSI Design
Actor: Hoang Bao Long

## Slide 42: 4. Verification Results

## Slide 43: 4. Verification Results

## Slide 44: 4. Verification Results

## Slide 45: 4. Verification Results

## Slide 46: 4. Verification Results

## Slide 47: Thanks for watching
Digital VLSI Design
Actor: Hoang Bao Long